## Slide 1: Overview
Dr M Shamim Kaiser
kaiser@juniv.edu

## Slide 2: Wireless Comes of Age
Guglielmo Marconi invented the wireless telegraph in 1896
  Communication by encoding alphanumeric characters in analog signal
  Sent telegraphic signals across the Atlantic Ocean Communications satellites launched in 1960s
Advances in wireless technology
  Radio, television, mobile telephone, communication satellites
More recently
  Satellite communications, wireless networking, cellular technology

## Slide 3: The Electromagnetic Spectrum

## Slide 4: The Electromagnetic Spectrum 2

## Slide 5: Different Wireless Technologies
Personal Area Networks: Bluetooth
Local Area Networks: Wifi
Metro and Wide Area Networks: Cellular
Satellite Networks
Sensor networks

## Slide 6: Different Network Characteristic

## Slide 7: Cellular Network Evolution

## Slide 8: Why Wireless?
Ease of use:
  Un-tethered use from anywhere
Ease of deployment:
  No running media cables between Transceivers
Mobility:
  Communicate while moving

## Slide 9: Challenges in the Wireless Domain
Inherently broadcast and shared
  Users can impact other users, just by co-location or location vicinity
  Limited capacity; no adding cables to add capacity
  Licensing of spectrum, or ‘collisions’ in unlicensed
Unpredictable Medium
  Medium is dynamic, even without devices moving
  Devices may be moving
  Attenuation with distance, multi-paths, higher error rates, and unpredictable channel responses
Device limitations, such as battery capacity or screen sizes
Politics and Incompatible standards

## Slide 10: Electromagnetic Signal
Signal: Electromagnetic (EM) field as a function of time
EM waves may travel in media such as space, air, glass, water etc.
Can equivalently also be expressed as a function of frequency
  Signal consists of components of different frequencies

## Slide 11: About Channel Capacity
Impairments, such as noise, limit data rate that can be achieved
For digital data, to what extent do impairments limit data rate?
Channel Capacity – the maximum rate at which data can be transmitted over a given communication path, or channel, under given conditions

## Slide 12: Concepts Related to Channel Capacity
Data rate - rate at which data can be communicated (bps)
Bandwidth - the bandwidth of the transmitted signal as constrained by the transmitter and the nature of the transmission medium (Hertz)
Noise - average level of noise over the communications path
Error rate - rate at which errors occur
  Error = transmit 1 and receive 0; transmit 0 and receive 1

## Slide 13: Nyquist Bandwidth
For binary signals (two voltage levels)
C = 2B
With multilevel signaling
C = 2B log2 M
where, M = number of discrete signal or voltage levels

## Slide 14: Shannon Capacity Formula
C=Blog2(1+ SNR)
Represents theoretical maximum that can be achieved
In practice, only much lower rates achieved
– Formula assumes white noise (thermal noise)
– Impulse noise is not accounted for
– Attenuation distortion or delay distortion not accounted for

## Slide 15: Example of Nyquist and Shannon Formulations
Spectrum of a channel between 3 MHz and 4 MHz ; SNR(dB) = 24 dB
B=4-3=1MHz
SNR (dB)=24dB=10log10(SNR), thus SNR=251
Using Shannon’s formula
C=8Mbps

## Slide 16
How many signaling levels are required?

## Slide 17: Transmission Media
Transmission Medium: Physical path between transmitter and receiver
Guided Media
– Waves are guided along a solid medium
– E.g., copper twisted pair, copper coaxial cable, optical fiber
Unguided Media
– Provides means of transmission but does not guide electromagnetic signals
– Usually referred to as wireless transmission
– E.g., atmosphere, outer space

## Slide 18: Unguided Media
Transmission and reception are achieved by means of an antenna
Configurations for wireless transmission
– Directional
– Omnidirectional

## Slide 19: General Frequency Ranges
Microwave frequency range
– 1 GHz to 40 GHz
– Directional beams possible
– Suitable for point-to-point transmission
– Used for satellite communications
Radio frequency range
– 30 MHz to 1 GHz
– Suitable for omnidirectional applications
Infrared frequency range
– Roughly, 3x1011 to 2x1014 Hz
– Useful in local point-to-point multipoint applications within confined areas

## Slide 20: Terrestrial Microwave
Description of common microwave antenna
– Parabolic "dish", 3 m in diameter
– Fixed rigidly and focuses a narrow beam
– Achieves line-of-sight transmission to receiving antenna
– Located at substantial heights above ground level
Applications
  – Long haul telecommunications service
  – Short point-to-point links between buildings

## Slide 21: Satellite Microwave
Description of communication satellite
– Microwave relay station
– Used to link two or more ground-based microwave transmitter/receivers
– Receives transmissions on one frequency band
(uplink), amplifies or repeats the signal, and transmits it on another frequency (downlink)
Applications
– Television distribution
– Long-distance telephone transmission
– Private business networks

## Slide 22: Broadcast Radio
• Description of broadcast radio antennas
– Omnidirectional
– Antennas not required to be dish-shaped
– Antennas need not be rigidly mounted to a
precise alignment
• Applications
– Broadcast radio
• VHF and part of the UHF band; 30 MHZ to 1GHz
• Covers FM radio and UHF and VHF television

## Slide 23: Multiplexing
Capacity of transmission medium usually
exceeds capacity required for transmission
of a single signal
Multiplexing
  carrying multiple signals on a single medium
  More efficient use of transmission medium

## Slide 25: Use of MUX
Cost per kbps of transmission facility declines with an increase in the data rate
• Cost of transmission and receiving equipment declines with increased data rate
• Most individual data communicating devices require relatively modest data rate support